## Slide 1: Coprocessor 0：MIPS Processor Control
邹旭
2018.8.13

## Slide 2: Function
CPU configuration (Chapter 10)
Cache control (Chapter 4)
Exception/interrupt control (Chapter 5)
Memory management unit control (Chapter 6)
Miscellaneous
Notes: Miscellaneous: Timers, event counts, parity error detection. Additional functions built into the CPU.

## Slide 3: CPU control instructions
Memory management implementation (Chapter 6)
Cache control (Chapter 4)
Register access
  mtc0/dmtc0 s, <n> #move to coprocessor 0, setting bits
  mfc0/dmfc0 d, <n> #move from coprocessor 0, inspecting bits
Undoing the effect of exception
  k0, k1 #general purpose registers($26, $27)
  #use in exception handler code
  eret #return to user mode & change the privilege level

## Slide 4: CPU control registers and their encoding
256 registers, 32-bit or 64 bit
$register number, select number
  $0, 0 means register 0, select 0
Individual CPUs may define extra fields in some registers.
Register mnemonic | CP0 register No. | Description
SR | 12 | Status Register
Cause | 13 | …
Config Config1-3 | 16 16.1-3 | …
… |  | 

## Slide 5: Registers relevant at certain circumstances
After power up
  SR, Config0-3
Handling any exception
  EPC, k0 k1, Cause
Returning from exception
  EPC, SR # user privilege, enable interrupts, SR(EXL)
Interrupts
  SR, Cause # interrupt mask
Instruction just there to cause exceptions (break, syscall)

## Slide 6: Status register
CU3-0 #coprocessor enable
  Set CU0: enabling user privilege programs to run CP0 instructions
  Set CU1: use FPU, Coprocessor 1 is the FPU
  Set CU2: systems builders can implement a CP2
  Set CU3: CP3 is not compatible with a standard FPU
RP #reduced power
FR #mode switch
RE #reverse endianness

## Slide 7: Status register
MX #enable for either DSP or MDMX ASE (instructions set extensions)
PX #64-bit instructions but still 32-bit addressing in user mode
BEV #Boot exception vectors (Section 5.3)
TS #TLB shutdown (Chapter 6), hardware reset
SR #soft reset
  Clear following a hardware reset
  Set after soft reset or NMI
NMI #nonmaskable interrupt

## Slide 8: Status register
IM7-0 #interrupt mask
  6 interrupt resources generated by signals from outside the CPU core
  2 interrupt resources are two software writable interrupt bits in the Cause register
KX, SX, UX #enable the much larger space available with a 64-bit CPU
KSU #CPU privilege level
ERL #error level, provide support for the cache error handler
EXL #exception level, forces kernel mode and disables interrupts
IE #global interrupt enable

## Slide 9: Cause register
What kind of exception happened and decide which exception routine to call
IV WP IP1-0 is writable, others read only
IP7-2, IP1-0 can cause interrupt according to SR(IM) bit
ExcCode tell you what kind of exception happened (5 bits, 32kinds)
  Syscall
  Overflow
  Trap
  …

## Slide 10: Configuration register
Config 0
  Specify various configuration and capabilities imformation
Config 1
  L1 I-cache & L2 D-cache & others
Config 2
  L2 cache & L3 cache
Config 3
  Other capabilities

## Slide 11: Processor ID (PRID) register
Company options
  Defined in CPU manual
Company ID
  Available from MIPS technologies
CPU ID
  Related with instruction set & CPU control register
Revision
  Keep track of silicon revisions

## Slide 12: Ebase and IntCtl: Interrupt and exception setup
Ebase
  the base address for the exception vectors
  relocate all the exception entry points for a CPU
IPTI && IPPCI
  Internal timer interrupt
  Performance counter overflow interrupt
VC
  Vector spacing

## Slide 13: Other registers
EPC: Exception restart address register
BadVAddr: Bad virtual address register
Count / Compare: the on-CPU timer
LLAddr: Load-linked address register

## Slide 14: CP0 Hazards
Execution hazards
  Happened when reading a CP0 register value
  ehb
Instruction hazards
  Happened at instruction’s very earliest stages
  jr.hb & jalr.hb replace subroutine return/call